## Slide 1: Energy Treasure Hunt INPLT – Kickoff
Dates

## Slide 2: Walt Brockway, PE, CEM
Owner, Brockway Consulting LLC
32 Years with Alcoa
    Engineer, Engineering manager, plant manager
5 years with GE Nuclear
Started the Alcoa EE program in 2002
Performed more than 30 Energy Treasure Hunts
Consulting with US Department of Energy, food, metals, pharma, building products.
Facilitator Bio

## Slide 3: Energy Treasure Hunt Exchange Overview

## Slide 4: What is an Energy Treasure Hunt?
  An Energy Treasure Hunt is a 3 - 5 day event that focuses on identifying day-to-day operational energy efficiency improvements.
  The process involves observing the facility during idle / partially idle time periods (frequently Sunday) to identify energy waste
Areas of Energy Efficiency Improvement
Operational Energy Efficiency Improvements
Turning off equipment when not in use
Changing set points
Automating shutdowns
Reducing load on the equipment
Recover wasted energy

## Slide 5: Energy Treasure Hunt Versus Energy Assessment
Treasure Hunt
Continuous process (repeat annually, quarterly . . . )
Internal resources
Focus on operational opportunities
Assessment
Standalone event (assess as needed)
External resources
Focus on system performance and technology
Treasure Hunts
Assessment
No Cost
Low Cost
Capital
Notes: The key difference between an energy Treasure Hunt and an assessment is the focus on no cost / low cost opportunities. Most Treasure Hunt savings come from operational behavior in a facility whereas assessments frequently encompass technological opportunities that involve capital.

## Slide 6: What is an Energy Treasure Hunt Exchange?
  An Energy Treasure Hunt that involves the exchange of energy teams between two facilities or companies.
Host Plant (Plant X)
Invited Plant
(Plant Y)
4~5 People
(DOE Facilitator)
BP Technical Account Manager
People from the host company’s other plants
Host Plant (Plant Y)
Invited Plant
(Plant X)
4~5 People
BP Technical Account Manager
People from the host company’s other plants
Event A
Event B
Energy Treasure Hunt Exchange Process as adopted by the Better Plants Program

## Slide 7: The Basic Mission
Assemble with your teams
Facility walk through for each team to generate ideas
Assess idea feasibility, gather data, quantify
At the end of each day the teams brief each other on what they will pursue
Notes: The basic task of an energy Treasure Huntis to generate ideas and quantify them. Many opportunities will be judged by the value they bring in energy savings and spending reduction. There are no bad ideas – quantify as many as you can, and let the plant determine whether or not they are worth pursuing after the Treasure Hunt. Due to the scope of no cost/low cost there is a high implementation rate of energy Treasure Hunt opportunities.

## Slide 8
All departments have a role to play in improving energy efficiency
    Successful energy programs are horizontal in an organization, not vertical
Energy treasure hunt draw participants from across all operations and from outside the host facility.
Production
Safety
Human Resources
Environmental
Energy
Maintenance
Procurement
Engineering
Projects
Participant Overview – Energy Treasure Hunt
From the Supply Chain Network
From within the Same Company
From other manufacturing companies, contractors
Host Site
Participants
State Representatives – Utility Representatives
Notes: Energy usage can be affected by everyone in an organization. It needs to be viewed as something all departments have a stake in to be successfully managed. Energy awareness should impact an organization similarly to environmental, health, safety, and human resources.

## Slide 9
  The event aims to educate all the participants on,
  What an energy treasure hunt exchange is, its value and benefits
  How to evaluate equipment energy use (both idle and non-idle times)
  How to identify equipment and process opportunities
  Methods for collecting energy data and common data collection tools
  How to effectively present outcomes of the treasure hunt
Learning Objectives – All Participants

## Slide 10: Learning objectives - Future Facilitators
Treasure hunt facilitation
How to select processes, plants, departments for treasure hunts
Use of diagnostic tools and techniques
The importance of Team makeup – processes and people
Prioritizing energy-saving opportunities
Replication across facilities, departments, business units
Preparation of treasure hunt outcome for management

## Slide 11: Overview – Treasure Hunt Exchange
A Treasure Hunt Exchange encompasses both training and a “hunt”
  Does not require sophisticated technical analysis
  Calculations are (relatively) simple
  Can be applied by employees of varying disciplines
  Train selected participants to facilitate future treasure hunts
A three day activity – at completion, the facility has sufficient information to execute identified opportunities and an employee who can facilitate future treasure hunts within the organization
Opportunities/ideas are solicited from many disciplines and can be replicated across similar processes and businesses
The Treasure Hunt process can be replicated and repeated (through this training)
Advantages of a Treasure Hunt

## Slide 12: Some Stats on Energy Treasure Hunts

## Slide 13: 90% of opportunities identified have < 1 year paybacks
Chart: Identified Opportunity
| Implementation Cost | Payback
< 1 Yr | 372332 | 2574846
< 2 Yr | 313856 | 193182
< 3 Yr | 91895 | 39801
Energy Treasure Hunt opportunities tend to be small, but economically competitive (shorter payback)

## Slide 14
55% of ideas generated are implemented
Chart: Opportunty Identified VS Savings Captured
| Plant 1 | Plant 2 | Plant 3 | Plant 4 | Plant 5 | Plant 6 | Plant 7 | Plant 8 | Plant 9 | Plant 10 | Plant 11 | Plant 12 | Plant 13 | Plant 14 | Plant 15 | Plant 16 | Plant 17 | Plant 18 | Plant 19 | Plant 20 | Plant 21 | Plant 22
Savings Identified | 468250 | 319804 | 441677 | 106096 | 347466 | 387568 | 125482 | 292747 | 208000 | 63000 | 192019 | 263759 | 41011 | 76052 | 933587 | 36352 | 798076 | 172580 | 193525 | 79152 | 40149 | 259165
DI2 Value Captured | 43000 | 215000 | 333000 | 132000 | 194000 | 131000 | 73000 | 234000 | 185000 | 87000 | 432000 | 104000 | 0 | 32918 | 385000 | 54000 | 261000 | 109000 | 18000 | 7000 | 124000
Identified –
Captured -

## Slide 15: Results from the Field
Chart: 
| Plant 1 | Plant 2 | Plant 3 | Plant 4 | Plant 5 | Plant 6 | Plant 7 | Plant 8 | Plant 9 | Plant 10 | Plant 11 | Plant 12 | Plant 13 | Plant 14
% savings | 15 | 4 | 6 | 5 | 5 | 5 | 10 | 7 | 3 | 3 | 10 | 9 | 17 | 10
Plants
% Energy Savings
Average Savings 8%
*The chart represents the %energy savings realized at 14 separate treasure hunt events run at Alcoa.

## Slide 16: Facility Information

## Slide 17: Plant Energy Use
Chart: ENERGY SPEND
Chart: 
| Electricity | Gas
Energy (MMBTu) | 2401309.2008 | 781941.2795

USE THIS SECTION TO ADD FACILITY INFORMATION FROM THE PRE- TRAINING DATA COLLECTED

## Slide 18: 2014 Annual Information Energy Rates
Electricity $0.05/kWh
Natural Gas $3.00/MMBTU
TOTAL: ~$ / year
Plant Energy Spend
Chart: Annual Energy Cost
Chart: 
| Electricity | gas
Energy Spend | 8305302.8 | 2345823.8384
USE THIS SECTION TO ADD FACILITY INFORMATION FROM THE PRE- TRAINING DATA COLLECTED
ADD ADDITONAL SLIDES IF NECESSARY
Notes: Many Treasure Hunt participants may be unfamiliar with their plant’s annual energy spend – Use this slide to familiarize them with the business impact energy usage has at their facility.

## Slide 19: Energy Treasure Hunt – Guidelines

## Slide 20: Basic Daily Format – Energy Treasure Hunt
Sunday – 8AM – 4PM
  Introductions, background information
  Training on best practices identification
  Training on use of diagnostic equipment
  Observe idle facility, generate ideas
  Daily flip-chart notes – major opportunities
Monday – 7AM – 5PM
  Training on use of DOE software tools and calculation sheets
  Observe facility under operation
  Investigate ideas, gather information
  Identify and complete top 2 detail sheets
  Complete presentation slides for top 2 detail sheets
Tuesday – 7AM – 4PM
  Finalize / review all detail sheets
  Findings summary
  Dry run through presentation / format
  Present to management
Sunday is typically a non-production day for many facilities. The Energy Treasure Hunt agenda is adjusted appropriately for plant hosting the event

## Slide 21: Weekend Demand / Fixed Usage
Weekend Demand
Notes: Fixed usage is the baseline amount of energy a facility needs when it is most idle. Utilities such as lighting, building security, compressed air, and heating and cooling, will be required 24/7 for a facility to remain functional for start-up and shut down. Energy Treasure Hunts typically target these baseline utilities and evaluate them for wasted energy. Questions to ask during a Treasure Hunts : can you get your idle production energy usage as low as your weekend demand / or holiday shut downs? Why do you use more energy on the off shift during the week vs. times when the plant is closed?

## Slide 22: Determine Focus Areas / Teams
Team 1
Team 3
Facilitator
& Host
Team 2
Examples of team focus areas. Select focus areas based on your facility.
(Target 3 teams of 5 participants)

## Slide 23: How do we approach a Treasure Hunt?
Tour the facility and observe operations
Identify opportunities and interview personnel
Gather data to evaluate and quantify opportunities
Complete opportunity sheets for each opportunity
Implement opportunities during the Treasure Hunt where possible!

## Slide 24: Observing The Idle Facility
Most important day for generating ideas
Rarely is production activity 24 hrs / 7 days a week
  Take note of maintenance downtime / shift changes / off shifts
Use your eyes and ears to find wasted energy!

## Slide 25: Fixed vs. Variable Energy Usage
Bldg & Security
Startup / Shutdown
Fixed
Variable
Energy
Volume
Volume
Control operating times
2) Automate shutdowns
3) Control temperature set points
4) Just in time operations
ENERGY
MINIMIZATION
Bldg & Security
Startup / Shutdown
Fixed
Variable
Energy

## Slide 26: Typical Treasure Hunt opportunities – Lighting
  Turn off excess lighting where possible. During a treasure hunt, experiment by turning off lights and then measuring the available lumens.
  At infrequently occupied areas, Implement shut down procedures or install occupancy sensors.
  Identify unnecessary lighting. Robots do not need light to work.
  Retrofit lighting with more efficient technology.
  LED can save more on maintenance than energy in some applications.

## Slide 27: Typical Treasure Hunt opportunities – Steam
  General steam leaks
  Broken Steam Traps
  Condensate leaks
  Boiler Tune up
  Poor or missing insulation
  Building heat with poor control

## Slide 28: Typical Treasure Hunt Opportunities –Compressed Air
  Operate at the lowest practical pressure set point
  Replace pneumatic energy with electrical energy where practical
  Evaluate high efficiency nozzles
  Eliminate inappropriate end use applications
  Optimize control strategy
  Perform a leak survey
  Install solenoid valves on open blowing
  No loss condensate drains
bag test on compressed air leaks!

## Slide 29: Typical Treasure Hunt opportunities - Exhaust
Exhaust systems frequently operate regardless of production requirements. Implement shut down procedures or automate shut down based on production processes.
  Fume hoods
  Scrubbers
  Dust collectors
  Extraction systems
  Chip collectors

## Slide 30: Typical Treasure Hunt opportunities – Process Heating
  Combustion tuning
  Combustion efficiency – burner upgrades, recuperators
  Poor furnace insulation
  Furnace shut downs / non-production management
    Temperature set points
    Recirculation fans / blowers
    Minimize ramp up time
    Excessive soak time

## Slide 31: Typical Treasure Hunt opportunities – Cooling / HVAC
Cooling Towers
  Match tower capacity with process requirements
    Less active cooling may be needed during night, colder seasons, and non production
  Check for throttled pumps / opportunities for VFD
HVAC / Makeup Air / Comfort Cooling
  Use programmable thermostats to optimize cooling schedule
    Particularly in non 24/7 areas such as offices, warehouses, partial production areas
  Challenge temperature set points
  Less makeup air may be needed during non production, if possible, shut down a few units

## Slide 32: Typical Treasure Hunt opportunities – Process Equipment
  Ensure auxiliary energy is minimized during non production
    Shut down lubrication pumps, valve off compressed air, consoles, lighting panels
  Production cells should have a shut down procedure during idle time
  If the process is not a bottleneck in plant production, consider batch processing and avoid constant idle time waiting for product
  Optimize throughput
    parts washers
    cooling tables / fans
    die heaters
    Extrusion machines

## Slide 33: Documentation using Opportunity Sheet
An opportunity detail sheet is a tool that helps organize and document information about identified opportunities
Each opportunity should have an individual “opportunity sheet”
Information captured
Description
Implementation costs
Energy Saved
Cost Savings
Payback Metrics

## Slide 34: Important instructions for opportunity sheets
Each team leader will be given a flash drive with a copy of a blank master opportunity sheet that is “read only”
For each opportunity open up the master opportunity sheet and “save as” the title of the opportunity.
  There will be a separate opportunity sheet for each opportunity your team identifies.
User inputs on the opportunity sheet are marked by green cells– do not modify non-user input cells, this can break the macros embedded in the spreadsheet or modify important formulas
You may append new blank worksheets or “tabs” in a detail sheet if you wish to do off sheet calculations or document further information

## Slide 35
Useful Resources

## Slide 36: Useful Resources
Energy Calculators
  To find “Energy Saved” for
  opportunity sheet
Handouts
  To help identify opportunity
Diagnostic Equipment
  To help collect accurate data
Tour the facility and observe operations
Identify opportunities and interview personnel
Gather data to evaluate and quantify opportunities
Complete opportunity sheets for each opportunity
The following resources are made available to help
participants with each step of the treasure hunt process

## Slide 37: Energy Calculators
  Two types of Energy Efficiency Calculators are available
  Treasure Hunt Calculators
      To estimate the savings associated with typical operational opportunities, e.g. Scheduling the equipment, reducing the load on the equipment etc.
  Opportunity Specific Calculators
      Available for some common opportunities that cant be easily quantified using the treasure hunt calculator e.g. Insulation, lighting replacement etc.
  Participants can use their own method or tool to quantify savings, however, the result of the calculation and description still needs to be captured in the standard opportunity sheet provided.
  To quantify the energy savings associated with an identified opportunity
  The results from the calculator are used to populate the opportunity sheets.

## Slide 38: Treasure Hunt Calculators
    Each energy source (and water) has its individual Treasure Hunt Calculator
All the treasure hunt calculators have three common steps
  Step 1: Determining operational time each year
  Step 2: Determine the rate of energy use
  Step 3: Determining consumption.
The calculators provide different ways to calculate “rate of energy use” depending on the energy source
The calculators are designed for ease of use
Energy Treasure Hunt Calculator– Electricity

## Slide 39: Energy Calculators - Suite
The following calculators are available as part of the toolkit and DOE is continuously working to improve the portfolio of calculators available.

## Slide 40: Data Gathering Tools
DOE provides energy diagnostic equipment and teaches the participants how to use them
Helps participants evaluate equipment performance and quantify energy performance improvement more accurately

## Slide 41
Handouts
  System specific handout sheets are provided by DOE to help participants identify and quantify energy savings opportunities.
  Three sets of handouts for each system type is available;
    System Checklist
    Data Collection Sheet
    System Cheat Sheet
  The handouts are not meant to be all encompassing
  Participants should only use the handouts as a tool to get started and not solely rely on it

## Slide 42: Handout 1 – System Checklist
  Checklist (things to look for sheet) help identify common opportunities
The handout provide a list of best practices
Typical system schematic is provided wherever applicable
A list of “things to check” is provided by system area
Checklist are available for
  Compressed air system
  Steam system
  Process heating system
  Chilled water system
  Pump and Fan system
  Lighting and
  Process Equipment

## Slide 43
Data Collection Sheet help collect the right data to quantify common opportunities
Handout 2 – Data Collection Sheets

## Slide 44
Cheat Sheets provide common “Rule of Thumb” for a system
Provide typical system performance information
Help participants estimate savings associated with commonly identified opportunities
Handout 3 – System Cheat Sheets
Cheat Sheet help to quickly estimate savings associated with common opportunities

## Slide 45: Summary
Walkthrough the facility and observe operations
Identify opportunities
Collect relevant data
Quantify Savings
Create Opportunity Sheet
Leverage available
Resources

## Slide 46: Questions / Comments

## Slide 47
Gather your teammates and head out !