## Slide 1: How to Find and Begin using MEASUR: The Manufacturing Energy Assessment Software for Utility Reduction

## Slide 2: DOE Industrial Software Tools
Designed to help energy and sustainability teams identify savings opportunities in their operational energy usage and emissions
Energy Systems
MEASUR
Electrification for Decarbonization
Compressed Air Scoping Tool
Energy Management
VERIFI
50001 Ready Navigator
Energy Footprint Tool
Plant Energy Profiler
Implementation Guidance Toolkit
Carbon, Water, & Waste
Plant Water Profiler
Plant Carbon Footprint & Decarbonization Assessment Tool
Carbon Emissions Calculator
Waste Stream Energy Content

## Slide 3: DOE Energy Efficiency Software
Technology and vendor agnostic tools to identify, quantify, and validate energy saving opportunities
  Original DOE software tools developed in the 1990’s in collaboration with industry experts
Modernize to Open-Source Software
  Single Free, Open-Source, OS Agnostic Tool
  Upgraded tool capabilities
  Government-side open-source software UT-Battelle Permissive License: “Do whatever, but please provide attribution.”
  Desktop/Web/Mobile
  Automatic update notification
Enable Technology Field Validation

## Slide 4: MEASUR is an Integrated Energy Tool
Free to Use
OS Agnostic
  Desktop: Web & App - Windows, Mac, Linux
  Mobile: Web & App – Android & iPhone
International Useability
  No limits on where they can be downloaded or accessed
  Google Translate available for web version
  Unit system flexibility: Make an assessment in metric or U.S. units and switch to the other
Data Privacy
  Data is stored on *YOUR* device
  No data you entered is sent to us unless you send it to us directly
    Data related to use (where you click, etc.) is collected via Google Analytics to improve the tool
  Automatic Updates

## Slide 5: How MEASUR can Help Assessments
Model manufacturing energy use and generation
Quantify savings opportunities
  Help reduce the losses in key manufacturing energy users ~4.48 QBTU (2018)
6 Assessment types, 2 Inventories, + Treasure Hunt
  Pumps, process heating, fans, steam systems, and compressed air
  Motor & Pump Inventories
  Treasure Hunt with calcs for all systems
80 Stand alone Calculators
  Pumps, fans, heating, compressed air, steam, motors, lighting, CHP, etc.

## Slide 6: Finding MEASUR
Officially released March 2022
Updates will occur often
  Automatic notification of updates if connected to the internet
  Please report bugs to measur-help@ornl.gov
Download from DOE or GitHub
  Uninstalling will delete your assessments!
If using online –
  Clearing cache will delete your assessments!
Download here:
https://www.energy.gov/eere/iedo/measur
https://ornl-amo.github.io/
Or Google “MEASUR”
Web version: https://measur.ornl.gov/

## Slide 7: MEASUR Demo
Using MEASUR

## Slide 8: Getting Started
Start an assessment
Create an inventory
View Assessment Dashboard
Use Properties & Equipment Calculators
Help and User Experience
  Change Settings
  View Tutorials
  Manage Custom Materials
  Provide Feedback
  Translate

## Slide 9: Dashboard – Assessments organized in folder structure
Move, copy, import and export assessments
Add/view facility information and folder-wide settings
Make pre-assessment screenings
Generate rollup reports of several assessments
Add New Assessment
Add New Inventory
Folders can represent Facilities or Departments

## Slide 10: MEASUR includes Help Text & Tutorials
Tutorials
  Help to get started using tool
Help text for each data entry field
  Diagrams to help understand where to obtain data
  Can switch between help or results being shown by default

## Slide 11: Customize Units
Units are easily customizable and can be changed after data entry!
Can be changed globally in Settings or for a folder

## Slide 12: Start an Assessment from the home page or dashboard
Choose a unique name for the assessment
Set Assessment type (Pump, Compressed Air, Fan, Process Heater, Steam, Treasure Hunt, Wastewater)
Choose folder location
  Or make a new folder
Several places to start an assessment

## Slide 13: Assessments all have similar workflow
Create a baseline
Enter data about current system setup
Create an assessment
Modify key variables to create What-if scenarios and compare
Review Results

## Slide 14: Treasure Hunt helps find low/no cost opportunities
Find low/no cost energy savings opportunities in motor systems, process heating, compressed air, lighting, etc.
Simplify report out with automatically built PowerPoint presentation
Get started right with automatically built Project Tracker (Excel)

## Slide 15: Simple, easy-to-use Calculators
80 Stand alone Calculators
  Motors
  Pumps
  Fans
  Process Heating
  Process Cooling
  Steam
  Compressed Air
  Lighting
  General
Most have graphical results

## Slide 16: Simple, easy-to-use Calculators
80 Stand alone Calculators
  Motors
  Pumps
  Fans
  Process Heating
  Process Cooling
  Steam
  Compressed Air
  Lighting
  General
Most have graphical results

## Slide 17: Things to remember
MEASUR is great for good estimations, but
Quality of results depends on the quality of data!
  Better baseline data, more accurate results
  More realistic modifications, more accurate results
  Keep in mind when pitching projects

## Slide 18: Starting an Assessment
Choose a unique name for the assessment
Set Assessment type (Pump, Compressed Air, Fan, Process Heater, Steam, Treasure Hunt, Wastewater)
Choose folder location
  Or make a new folder

## Slide 19: Each System Setup starts with Assessment Settings
Decide settings for Assessment
  Units: Imperial or Metric
  Can set Energy Results separately
Select energy source for furnace
  Cannot be changed if there are losses in Heat Balance
Add notes on conditions at time of assessment

## Slide 20: System Setup
Start with current equipment and operations - Baseline
Assessment Settings: Set units and basic assessment settings
Assessment Specific Tabs
  Data Entry for baseline assessment
  Intermediate Results
  Help text for each data entry field

## Slide 21: Assessments
Explore Opportunities: build scenarios from pre-established energy savings measures
Modify All Conditions: build scenarios using same forms as baseline
  Badges and field highlighting for visual cues
Explore energy savings opportunities

## Slide 22: Reports
View side-by-side comparison of all scenarios and graphs for data visualization

## Slide 23: Reports - Printing
Print to PDF for Assessment Reports & Rollup Reports

## Slide 24: MEASUR’s Modules
Pumps
Process Heating
Fans
Steam
Compressed Air
Wastewater
Treasure Hunt
Data Explorer
Inventories (Motors & Pumps)

## Slide 25: Pumps
Estimate motor full load amps, load current and power factor, fluid head, and fan and motor efficiency
Explore the savings from changing pump and motor efficiency (which can be optimized automatically), flow and head, or even fluid temperature

## Slide 26: Process Heating
Calculate heat losses from several heater components
Explore the savings from reducing flue gas oxygen or temperature, preheating air or charge materials, controlling furnace pressure, closing openings, etc.

## Slide 27: Fans
Estimate motor full load amps, load current and power factor, pressure and flow from a traverse analysis, and fan and motor efficiency
Explore the savings from changing fan and motor efficiency (which can be optimized automatically), flow and pressure, or even fluid characteristics

## Slide 28: Steam
Determine steam flows, fuel use, electricity production throughout system
Explore the savings from adding/removing turbines, adding flash tanks, increasing condensate recycle, etc.

## Slide 29: Compressed Air
Develop a compressed air inventory and understand average hourly operations, performance and impact on energy use
Explore the savings from reducing leaks, air demand, or system pressure, improve controls, etc.

## Slide 30: Wastewater
Determine sludge production, O2 supply and demand, MLSS or SRT, and aerator energy use
Explore the savings from optimizing SRT, reducing DO concentration, matching oxygen supply and demand, optimizing aerator performance, etc.

## Slide 31: Treasure Hunt
Find low/no cost energy savings opportunities in motor systems, process heating, compressed air, lighting, etc.
Simplify report out with automatically built PowerPoint presentation
Get started right with automatically built Project Tracker (Excel)

## Slide 32: Data Explorer
Two Key Functions
  Day Type Analysis
    Used for finding hourly averages for similar load profiles
    For Compressed Air Assessment and other long-term analyses
    Based on LogTool
  Data Visualization – easy graphing capabilities to explore large datasets

## Slide 33: Equipment Inventories
Modeled after MotorMaster
Record key information about equipment in one place
  Motors – Beta
  Pumps, fans, compressors, maintenance - Planning
Sort & filter, summary graphs, inventory printouts
Batch analysis for simple calculators

## Slide 34: Backup & Feedback
Easily backup entire MEASUR data
  If using downloaded version, can setup Automatic Backup
Let us know if you like MEASUR!
  Built in survey!
Bug Reporting
  Email: measur-help@ornl.gov
  Screenshots please

## Slide 35: Settings
Set global units & utility costs
Turn on/off Tutorials
Clear Data

## Slide 36: Dashboard – Set Facility Information
The Dashboard is designed to treat each folder like a facility or business unit
Enter information about facility. This will appear in reports
Set units and utility costs for any NEW assessments created
Quick Summary of all assessments in folder

## Slide 37: Dashboard - Pre-Assessments
Pre-Assessments are to help you triage equipment to best utilize assessment time
Switch between Energy Use and Cost if equipment uses different fuel
Graphed to quickly see most impactful
Enter either design specifications or meter data to determine your priorities

## Slide 38: Dashboard - Rollup Reports
Create Rollup Reports to see the impacts of opportunities on overall energy use
Then Click
View Equipment Summary
Review all reports
Choose which assessments & pre-assessments to include in rollup
Choose which scenario to include

## Slide 39: Example Calculators
O2 Enrichment
Motor Performance
Pump Curve
Compressed Air Leak Survey
Saturated Properties
CO2 Savings

## Slide 40: Custom Materials for fuels, charge materials, etc.
Add Fuels, Charge Materials, etc. that are not in MEASUR’s databases to reuse later
Can import & import custom materials

## Slide 41: About & Acknowledgements
About
  Intended Users
  Inputs/Outputs for each modules
Acknowledgements
  The end credits

## Slide 42: Release Notes
Gives brief overview of what has been added since last update
Can also look at before installing update

## Slide 43: Coming Soon
Water Diagram & Balance
Process Cooling
More Equipment Databases
  Modeled after MotorMaster+ Database
  Keep inventory of equipment (pumps, fans, compressors, etc.) connected to assessments

## Slide 44: Acknowledgements
Subject Matter Experts
Don Casada, Diagnostic Solutions, LLC, developed the original PSAT and FSAT, and contributed the algorithms for the Pumping and Fan modules.
Arvind Thekdi, E3M, Inc. developed the original PHAST and continued to contribute to the Process Heating module by providing the algorithms for the previous versions (PHAST 3.0 and PHASTEx), updating the algorithms for improved accuracy, and providing feedback.
Vern Martin, Donovan Martin, and Mats Falk, Flowcare, provided updated Fan algorithms and feedback during the development of the Fan module.
Ron Wroblewski, Productive Energy Solutions, reviewed and provided updated Fan algorithms for the Fan module.
Greg Harrell, Milligan University, developed the previous versions of DOE steam tools and continued to contribute to MEASUR by providing feedback.
Glenn Cunningham, Tennessee Technical University, reviewed and provided feedback for the Pump, Fan, and Steam modules, as well as many calculators.
Riyaz Papar, Hudson Tech., reviewed and provided feedback for the Steam module.
Walt Brockway, reviewed and provided feedback for the Treasure Hunt module.
Larry Moore, University of Memphis, developed the original Bio-Tiger model for Wastewater Treatment facilities, oversaw updates to the algorithm, and provided feedback during the development of the Wastewater module.
Frank Moskowitz, Draw Professional Services, reviewed and provided feedback for the Compressed Air module.
Eric Bessey, TTed Solutions, Inc, developed and provided updated algorithms from the originals AirMaster+ software , provided feedback during the current algorithm development
Eric J. Wahlberg, Wastewater Technology Trainers, reviewed and provided feedback for the Wastewater module and calculators.
ORNL Staff
SULI, CCI, URSI Participants
Kyle Beanblossom Kai Chen
Autumn Ferree Zach Fontenot
Allie Ledbetter
Jordan Lees
Charlotte Merchant
Ben Rappoport Raul Rios
Shiva Saravanan
Andrew Worley
Gina Accawi
Kristina Armstrong
Mark Root
Thomas Wenning
Alexandra Botts
Contractors and ORAU Student Employees
Nick Blondheim
Rachel Stone
Colin Causey
Jeff Jensen
Jon Hadden Dmitry Howard Michal Kaminski
Shubham Kokul
Subhankar Mishra Asha Shibu Preston Shires David Vance Michael Whitmer
Ahmad Abbas
Omer Aziz
Subodh Chaudhari
Kita Cranfill Daryl Cox Wei Guo
Chris Price Sachin Nimbalkar
Senthil Sundaramoorthy
Kiran Thirumaran

## Slide 45: Feedback or bugs? Email: armstrongko@ornl.gov accawigk@ornl.gov wenningtj@ornl.gov